## Slide 1
FR1 – Identification, authentication and access control
FR3 – System Integrity
FR2 – Use Control
FR7 – Resource Availability
FR4 – Data Confidentiality
FR5 – Restrict Data Flow
FR6 – Timely response to event
FR 5 – From
IEC 62443

## Slide 2
Introduction
• Importance of data flow control in Industrial
Control Systems (ICS)
• Segmentation of control
system architecture into
zones and conduits
• Alignment with the Purdue model's logical separation
approach

## Slide 3
Purdue Model
The primary requirement for data flow control is to prevent unnecessary and
undesired communication
between different parts of
the control system.

## Slide 4
Purdue Model
Following the principles of the Purdue model, we can determine the appropriate
zones within the control
system architecture.

## Slide 5
Scenario:
Manufacturing
Plant Hierarchy:
• Illustrating zones: Process
Control, Supervisory Control,
HMI, Corporate Network
• Variability in criticality and sensitivity across zones

## Slide 6
Firewalls
VLAN (Virtual LAN)
Unidirectional Gateways (Data
Diodes)
Data Flow
Control
Technologies:

## Slide 7
Stricter access controls and prevention of unauthorized communication
Enhanced data confidentiality and security
Efficient collaboration and communication
within control environment
Regulatory compliance and stakeholder
confidence
Benefits of
Effective Data
Flow Control

## Slide 8
Firewalls
• Guardians of zone boundaries
• Enforce predefined rule sets
• Control incoming and outgoing traffic based on IP, protocols, and ports
• Prevention of unauthorized data flow between zones

## Slide 9
VLAN (Virtual LAN)
• Logical network separation within a single physical infrastructure
• Each VLAN operates as an isolated network • Controlled communication between VLANs • Ideal when physical separation is not feasible

## Slide 10
Unidirectional Gateways
(Data Diodes)
• Establish one-way flow of information between zones
• Enables secure transmission from high-security to low-security zones
• Prevents reverse communication
• Sharing critical data without compromising security

## Slide 11
Implementation
When implementing data flow control, it is essential to consider the criticality of systems and the potential impact of any disruptions.

## Slide 12
Determine criticality
and sensitivity of zones
Implement VLANs for
logical separation
Deploy unidirectional
gateways for one-way
data transmission
Strategically place
firewalls at interaction
points
Implementation Strategy

## Slide 13
Significance of data flow control in ICS security
Strengthened security posture
through effective implementation
Optimized collaboration while ensuring
confidentiality and compliance
Wrap
Up